## Slide 1
SARCATHON 2026 · SEMICON HACKATHON
AXI4-Stream to
PCIe 6.0 Bridge
RTL integration, Vivado optimisation and SKY130 implementation
Team RoboKnights
Aditya Jain · Swaray Agrawal · Kshitij Seshadri
24 October 2026
SKY130 interconnect layout view
FPGA: Xilinx xcu250 | ASIC: SkyWater SKY130A
Notes: Title (≈ 40 s) · Aditya
*[Title slide on screen]*
> Good morning. We're Team RoboKnights: I'm Aditya, with Swaray and Kshitij.
>
> Our project is an RTL bridge that takes data from two FPGA-fabric producers — a SmartNIC and an ML inference accelerator, each on a 512-bit AXI4-Stream port — and delivers it into host memory over a PCIe 6.0 Flit-mode link.
>
> The design is split into three layers, one per person:
> - I built the interconnect: the two ingest ports, the arbiter and the clock crossing.
> - Swaray built the link layer: TLPs, Flits, CRC and FEC, and replay.
> - Kshitij built the protocol-to-PHY layer: the PAM4 lanes, link training, resets, config space, BAR0 registers and MSI-X interrupts.
>
> We took it to FPGA timing closure on a Xilinx Alveo U250 part, and through the open-source flow to GDSII on SkyWater 130 nanometre.
*[Point to the layout image]* This is the interconnect layout from that flow.

## Slide 2
RoboKnights / SARCathon 2026
02
Round 1 — RTL development and initial verification
By 15 October, the three layers passed their unit tests and were connected in a first system-level loopback.
AXI4-Stream → PCIe 6.0 Bridge | Round 2 technical review
2 / 10
Interconnect
Aditya
•
Dual 512-bit AXI4-Stream ingest ports
(SmartNIC and ML).
•
Weighted arbitration, session / offset
tracking and async FIFO.
•
Four RTL bugs fixed; 128/128 checked
beats, zero errors.
Link layer
Swaray
•
Write and replay buffers, 256-byte Flit
framing, DLLP parsing.
•
CRC/FEC and TLP-related blocks
individually unit-tested.
•
Transaction blocks not yet wired into the
complete path.
Protocol / PHY
Kshitij
•
Gray/PAM4 lane mapping and logical PHY
loopback.
•
Reset, configuration, MSI-X and sideband
controls.
•
4/4 initial cocotb tests passed; lane proofs
checked.
Status at submission
Connectivity was demonstrated; end-to-end TLP data correctness, complete address handling and link-to-PHY
backpressure remained open.
Notes: Round 1 (≈ 50 s) · Aditya
> In Round 1, up to 15 October, each of us built and unit-tested our own layer.
>
> *[Left column]* The interconnect was complete. We fixed four real bugs, including an arbiter deadlock and a combinational loop in the FIFO's full flag, and the integration bench passed 128 out of 128 beats.
>
> *[Middle column]* The link layer's core blocks — write buffer, replay buffer, Flit framing — were working and unit-tested, but the transaction blocks weren't yet wired into one path.
>
> *[Right column]* The PHY lane chain was bit-exact in loopback, the reset, config and MSI-X control plane existed, and 4 out of 4 cocotb tests passed.
>
> *[Bottom bar]* So at the Round 1 submission the layers were connected, but we hadn't yet shown data correctness end to end: there was no TLP packetizer, and no back-pressure between the link and the PHY. Round 2 started there.

## Slide 3
RoboKnights / SARCathon 2026
03
Round 2 — full integration and regression testing
Closed the gaps between the three RTL layers before committing to FPGA performance optimisation.
AXI4-Stream → PCIe 6.0 Bridge | Round 2 technical review
3 / 10
Simplified data path
ch0: SmartNIC
ch1: ML accel
interconnect_top
512-bit AXI4-S · WRR · sessions · CDC
link_layer_top
TLP → Flit · CRC/FEC · ACK/NAK replay
pcie_phy_top
PHY FIFO · PAM4 / Gray logical lanes
PCIe 6 logical link
What changed
•
Link-to-PHY FIFO and explicit ready / backpressure.
•
Shared TUSER definition; host BAR0 registers and address translation.
•
TLP packetisation, ACK/NAK replay and link-down recovery.
•
Corrected malformed TLP, overflow, CRC/FEC and cross-layer data-loss cases.
Verification at the Round 2 cutoff
144/144
TLPs delivered in Step 1 integration test
73/73
Required coverage bins across 40 random seeds
4/4
Formal proofs completed
46
Protected-code regression guards
Notes: Round 2 integration (≈ 70 s) · Kshitij
> Round 2 started with an honest review of the merged repository: all three layers in one tree, one layer at a time.
>
> It found real problems:
> - the layers didn't even compile together, because one module was defined twice;
> - the link layer's replay buffer had no ACK source, so it stopped after 31 beats;
> - the PHY drained data 32 times slower than the link wrote it, with no ready signal between them;
> - the TUSER bits between the interconnect and the link were in a different order, so every beat was routed as channel 0.
>
> *[Point to the diagram]* We fixed those layer by layer.
> - A FIFO and an explicit ready signal between link and PHY.
> - One shared TUSER definition, so the layout can't drift again.
> - Host BAR0 registers for the per-channel base addresses and limits.
> - ACK/NAK replay, and recovery when the link goes down.
>
> On the PHY side we also made the link train itself over the lanes — Detect, Polling with TS1, Configuration with TS2, then L0 — with lane deskew and lane-reversal detection, instead of being told it was trained.
>
> *[Point to the numbers]* The checkpoint at the end of this step:
> - 144 out of 144 TLPs delivered end to end in the integration test.
> - Then CI with 46 protected-code guard rules.
> - A randomized bench over 40 seeds hitting all 73 required coverage bins.
> - 4 formal proofs with SymbiYosys.
>
> Across Round 2 that came to 44 design bugs and 21 testbench bugs, each one tracked in our ledger with who found it, who fixed it and which patch carries it.

## Slide 4
RoboKnights / SARCathon 2026
04
Vivado synthesis — generated bridge schematic
Structural connectivity view from Vivado for bridge_top; shown as synthesis evidence, not a timing or post-route result.
AXI4-Stream → PCIe 6.0 Bridge | Round 2 technical review
4 / 10
How to read the figure
Hierarchy
The synthesized bridge_top view
contains interconnect_top,
link_phy_bridge_top and
reset/control structures.
Visible interfaces
AXI4-Stream data/keep/valid-
ready, BAR0/config, link status,
reset and PHY lane signals.
Interpretation
Generated netlist connectivity;
functional and timing claims are
supported separately by testbench
and Vivado reports.
Source: synth_design_schematic(1).pdf · Vivado Nlview, bridge_top · October 24, 2026
Notes: Vivado schematic (≈ 30 s) · Swaray
> This is the synthesized netlist of the whole bridge from Vivado. It isn't a timing result; it's evidence that the full hierarchy synthesizes as one design.
>
> *[Right panel]* You can see `interconnect_top`, the link-and-PHY block and the reset structures, with the AXI4-Stream, BAR0 and lane interfaces at the boundary. The functional and timing claims are backed separately by the testbenches and the Vivado reports on the next slides.
*(Keep this short — it's a visual check, not a talking slide.)*

## Slide 5
RoboKnights / SARCathon 2026
05
Vivado — timing progression across the optimisation runs
PCIe clock target: 250 MHz (4.0 ns) on xcu250, Vivado 2026.1.
AXI4-Stream → PCIe 6.0 Bridge | Round 2 technical review
5 / 10
0
50
100
150
200
250
PCIe Fmax (MHz)
250 MHz target
39
Initial
118
Step 4
base
49
Wave
A+B
147
Wave C
248
Freeze
255
Final
What the timing reports
showed
118 → 49 MHz
Widening the datapath created an
unrolled 51-level CRC-64 critical
path.
Recovery
Split CRC computation, constant-
mask XOR trees, pipelined RX
processing and decoupled
TREADY logic.
19,046 → 0
failing endpoints (Step 4 base → final)
Notes: Timing progression (≈ 70 s) · Swaray
> This chart is the story of our clock speed. The target is 250 MHz on the PCIe clock.
>
> *[Point along the bars]*
> - The very first build ran at 39 MHz.
> - After the integration fixes we had a clean, fully verified base at 118 MHz.
> - Then we did the obvious thing for throughput and widened the datapath to 512 bits end to end — and Fmax dropped to 49 MHz.
>
> We didn't hide that. The timing report showed exactly why: the CRC-64 over the whole Flit had become one combinational cone, 51 logic levels in a single cycle.
>
> So we split the CRC into per-chunk parts that are combined, which got us to 147 MHz. We then rewrote CRC and FEC as constant-mask XOR trees and registered the inbound beat, which got us to 248 MHz at the freeze. The last step, to 255 MHz, came from a fix the ASIC flow forced on us, on the next slide.
>
> *[Bottom line]* Failing timing endpoints went from 19,046 to zero.

## Slide 6
RoboKnights / SARCathon 2026
06
RTL changes that mattered most
Widen the datapath for throughput, pipeline it for clock speed, then fix the protocol so no data is lost.
Bottleneck
RTL change
Measured result
32-bit TX serialiser, one TLP per Flit
512-bit tlp_tx_wide engine; merges beats into Max-Payload TLPs,
split at 4 KB
ML 0.06 → 6.17 GB/s
about 100×
RX decoded 1 DW per clock; PHY
32× slower than link
16-DW/clock RX delimiter; wide PHY (8 B/lane/clk) with FIFO
back-pressure
NIC p99 58 → 0.59 µs
4.84 Mpps SmartNIC IMIX
CRC-64/FEC: 51 logic levels in one
cycle
Pipelined check; CRC/FEC as constant-mask XOR trees
49 → 248 MHz
TKEEP → popcount → limit →
TREADY: 27 ns
TREADY independent of TKEEP; near-limit beat checked one
cycle later (X.1)
255 MHz, all paths met
ASIC slack −12 → −0.5 ns
Replay never ACKed, FEC couldn't
correct, link hung on cable pull
ACK/NAK replay, SEC-DED FEC + CRC-64, credit flow control,
link recovery (K6)
Zero data loss
1,069 errors corrected, 7 cable pulls recovered, 40 random
seeds
Overall
118 → 255 MHz (2.2×) with 2% more LUTs, because the wide path replaced the serial one rather than adding to it.
AXI4-Stream → PCIe 6.0 Bridge | Round 2 technical review
6 / 10
Notes: RTL changes that mattered most (≈ 100 s) · Swaray + Kshitij
> Here are the five changes with the biggest measurable result, each with its number. The pattern is: widen the datapath for throughput, pipeline it for clock speed, then make the protocol lose nothing.
*[Row 1 — Swaray]*
> The old design squeezed 512-bit beats through a 32-bit serialiser and put one TLP in each Flit. We made the TLP engine as wide as the bus and merged beats into max-payload TLPs that never cross a 4 KB boundary. ML throughput went from 0.06 to 6.17 gigabytes per second — about 100 times.
*[Row 2 — Kshitij]*
> Receive and PHY had to keep up with the wider transmit side, or the latency would just move downstream. The RX now decodes 16 DWs per clock instead of one, and the PHY moves 8 bytes per lane per clock instead of one byte per four clocks, with FIFO back-pressure so nothing is dropped. SmartNIC tail latency went from 58 to 0.59 microseconds, at 4.84 million packets per second.
*[Row 3 — Swaray]*
> Widening first dropped us to 49 MHz, because CRC-64 became one huge cycle. Splitting it into XOR trees got us to 248.
*[Row 4 — Aditya or Swaray]*
> On the ASIC slow corner, the path from TKEEP through a popcount and the limit compare to TREADY took 27 nanoseconds. We made TREADY independent of TKEEP and check only a beat near the session limit one cycle later. That fixed the ASIC slack, from −12 to −0.5 nanoseconds, and it also gave the FPGA its last margin: 255 MHz with every path met.
*[Row 5 — Kshitij]*
> Speed means nothing if data is lost. The replay buffer now really gets ACKs and NAKs, FEC actually corrects, there's CRC-64 and real credit flow control, and the PHY recovers when the cable is pulled. Over 40 random seeds the bench corrected 1,069 errors and recovered from 7 cable pulls with zero data loss. These fixes came from a random test bench that reaches every error path.
*[Footer]*
> Overall: 118 to 255 MHz, 2.2 times faster, with only 2% more LUTs, because the wide path replaced the serial one instead of being added next to it.
*(If time is short: rows 3 and 4 are the strongest for judges. Something broke, we measured why, and we fixed it.)*

## Slide 7
RoboKnights / SARCathon 2026
07
Final FPGA results and workload measurements
FPGA specifications are from the final X.1–X.4 ledger; workload results come from RTL simulation.
AXI4-Stream → PCIe 6.0 Bridge | Round 2 technical review
7 / 10
Final FPGA implementation (xcu250)
Parameter
Step 4 base
Final
PCIe Fmax
118 MHz
255 MHz
AXI Fmax
—
221 MHz
WNS @ 4 ns
−4.439 ns
+0.072 ns
CLB LUTs
56,043
57,245
Flip-flops
24,482
39,269
Failing endpoints
19,046
0
Traffic results (simulation only)
Workload / metric
Base
Optimized
ML tensor throughput
0.061 GB/s
6.17 GB/s
SmartNIC IMIX rate
0.15 Mpps
4.84 Mpps
64 B packet rate
0.48 Mpps
11.6 Mpps
NIC IMIX p99 latency
58 μs
0.59 μs
NIC p99, ML 1:7
241 μs
4.2 μs
Resource note
BRAM / URAM / DSP = 0. Separate supplied synthesis report: 57,184 LUTs, 39,225 FFs; tool power estimate 3.499 W (medium confidence).
Notes: Final FPGA results and workloads (≈ 70 s) · Aditya
> *[Left table]* Final FPGA numbers on the xcu250:
> - PCIe clock 255 MHz with worst negative slack +0.072 ns; AXI clock 221 MHz.
> - Zero failing endpoints.
> - LUTs barely moved: 56k to 57k.
> - Flip-flops went up because of the pipelining — that's the deliberate trade.
>
> *[Right table]* Fmax alone doesn't tell you whether the bridge serves its two users, so we built our own traffic analyser and ran real workloads in simulation, normalised to 250 MHz:
> - ML tensors: 0.06 to 6.17 GB/s.
> - SmartNIC IMIX packets: 0.15 to 4.84 million per second.
> - Back-to-back 64-byte packets: 0.48 to 11.6 million per second.
> - NIC p99 latency: 58 to 0.59 microseconds.
> - With the ML stream saturating the link at a 1:7 weighting, the NIC's p99 still drops from 241 to 4.2 microseconds. That's the weighted arbiter doing its job.
>
> *[Resource note]* No block RAM, URAM or DSP is used: every buffer is LUT RAM, about 3% of the device.
>
> To be clear, these workload numbers are RTL simulation, not board measurements.

## Slide 8
RoboKnights / SARCathon 2026
08
SKY130 — physical implementation status
Reported status on 24 October 2026; interconnect GDSII completed, full-bridge physical sign-off not confirmed.
AXI4-Stream → PCIe 6.0 Bridge | Round 2 technical review
8 / 10
Layout view 1 · dense cell/routing display
Layout view 2 · metal/routing display
Interconnect (completed)
1.20 mm² die · 41% utilization · ~49k cells · 104 mW
DRC/LVS/antenna clean; hold met. Slow-corner setup −0.95 ns.
Full bridge (open)
≈3.9 mm² standard-cell area at narrow-profile synthesis.
Routing/sign-off not yet demonstrated. X.1 later improved interconnect setup to
−0.52 ns without new GDS stream-out.
Notes: SKY130 physical implementation (≈ 60 s) · Aditya
> We also took the design through LibreLane on SkyWater 130 nanometre.
>
> *[Left]* The interconnect went all the way to GDSII:
> - DRC, LVS and antenna clean, hold met.
> - 1.20 square millimetres at 41% utilisation, about 49,000 cells, 104 milliwatts.
> - Setup at the slow corner was −0.95 nanoseconds, which our X.1 fix improved to −0.52.
>
> *[Right]* For the full bridge we built a narrow ASIC profile from the same RTL: narrow PHY, smaller buffers, 30-nanosecond clock.
> - It went through synthesis, floorplan, placement, clock tree and global routing, about 3.9 square millimetres of cells.
> - Detailed routing didn't converge before the cutoff, so we're not claiming full-bridge sign-off.
>
> *(The reason is on the next slide.)*

## Slide 9
RoboKnights / SARCathon 2026
Why full-bridge GDSII was not completed by submission
The limiting factors were physical-implementation complexity, available compute and the submission window.
AXI4-Stream → PCIe 6.0 Bridge | Round 2 technical review
1. RTL and performance target
Wide 512-bit processing, parallel CRC/FEC,
replay buffering and pipelining supported
high simulation throughput with error-free
delivery in the tested cases. Such a datapath
also makes ASIC synthesis, placement and
routing more demanding.
2. ASIC flow and compute
The SKY130 flow exposed Yosys
latch/logic-loop issues in the RX correction
path and long full-design runs. We made
X.1–X.4 ASIC-compatibility fixes and
introduced a narrow, parameterized
implementation profile.
3. Timing of the final runs
Our initial computing resources were
insufficient to complete the full physical-
design runs within the available time.
Higher-capacity campus compute was
identified and secured, but debugging and
reruns extended into the submission
deadline.
Evidence at cutoff
Interconnect GDSII generated and DRC/LVS/antenna checks clean; full bridge synthesized (~3.9 mm² of
standard cells), but full-bridge routing and sign-off remained open.
Latest team-reported RTL simulation: 6.71 GB/s with zero observed data mismatches; earlier documented result: 6.17 GB/s. Final FPGA timing: 255 MHz and positive WNS
(+0.072 ns).
09
9 / 10
Notes: Why full-bridge GDSII wasn't completed (≈ 60 s) · Aditya
> We want to be upfront about what we didn't finish, and why.
>
> 1. The design itself. The same wide 512-bit processing, parallel CRC/FEC and replay buffering that gave us the throughput also make placement and routing much harder.
> 2. The ASIC flow. It exposed Yosys latch and logic-loop issues in the RX correction path that the FPGA tools never complained about. Our patches X.1 to X.4 fixed those, and we created the narrow implementation profile.
> 3. Compute and time. Our first machines didn't have enough memory for full-design routing. We secured campus compute, but debugging and reruns ran into the deadline. The router ran out of memory once, and on the restart the violations grew instead of falling, which tells us the floorplan is too congested. The next step is a looser floorplan, around 20% core utilisation, with capped router threads.
>
> *[Evidence bar]* At the cutoff:
> - Interconnect GDSII generated and clean.
> - Full bridge synthesized at about 3.9 mm², with routing and sign-off still open.
> - FPGA at 255 MHz with positive slack.
> - The latest team-reported RTL simulation shows 6.71 GB/s with zero data mismatches.
>

## Slide 10
RoboKnights / SARCathon 2026
Engineering decisions beyond a basic RTL bridge
What we actually implemented and tested—not claims of industry-first functionality.
AXI4-Stream → PCIe 6.0 Bridge | Round 2 technical review
1.
Two workloads on one fabric
Programmable weighted arbitration shares the link between
SmartNIC traffic and ML tensor streaming, with independent channel
sessions.
2.
Actual application-level profiling
An in-house analyzer tested IMIX traffic, ML tensors, mixed weights,
4 KB crossings, packet rate and latency—not just Fmax.
3.
Design for recoverability
ACK/NAK replay, CRC/FEC correction, link-drop/retrain cases,
resets, overflow and error injection were exercised.
4.
Regression protection
46 guard checks and a 40-seed randomized suite helped prevent
repaired cross-layer bugs from reappearing during optimization.
5.
Measured optimization trade-offs
We documented the 118 → 49 MHz timing regression, traced its
CRC-64 critical path and recovered to 255 MHz.
6.
Two technology profiles
Wide FPGA configuration and resource-reduced SKY130
configuration share RTL, with Yosys-safe logic for ASIC experiments.
Remaining engineering work
Full-bridge SKY130 sign-off, complete I/O timing constraints and improved heavy-noise throughput.
10
10 / 10
Notes: Engineering decisions (≈ 70 s) · Kshitij
> To close: six things go beyond a basic RTL bridge. These are what we actually built and tested, not claims of anything industry-first.
>
> 1. Two workloads on one fabric. A programmable weighted arbiter shares the link between SmartNIC packets and ML tensors, each with its own session, base address and limit.
> 2. Application-level profiling. Our analyser measures packet rate, tail latency, tensor throughput, 4 KB crossings and mixed weights, not just Fmax.
> 3. Design for recoverability. ACK/NAK replay, FEC correction, overflow handling, hot reset and link-down retrain are all exercised by tests. On the PHY, the link now sends logical idle when it has no data, so a silent lane really means a dead link. The training state machine leaves L0 on signal loss, lost framing or the partner retraining, resets the datapath cleanly and retrains, in about 1,700 clocks.
> 4. Regression protection. At one point two fixes were applied to stale copies of files and nine earlier fixes were silently lost. After that we added 46 guard rules that fail CI if an earlier fix disappears, plus the 40-seed randomized suite.
> 5. Measured trade-offs. We documented the 118-to-49 MHz regression, traced it to CRC-64 and recovered to 255.
> 6. Two technology profiles from one RTL. A wide FPGA configuration and a resource-reduced SKY130 configuration, with Yosys-safe logic for the ASIC.
>
> *[Bottom bar]* What's left: full-bridge SKY130 sign-off, complete I/O timing constraints, and better throughput under heavy channel noise.
>
> Thank you. We're happy to take questions.